CIRCUIT AND SYSTEM / SIGNAL PROCESSING CHAPTER

AEROSPACE & ELECTRONIC SYSTEMS/TECHNOLOGY MGMNT CHAPTER

Present

Elimination of Out-of-Band Quantization Noise in Direct Digital-to-RF Transmitters

a technical talk by WALID K. M. AHMED, Senior Member IEEE

## October 28th, 2008; 6 PM at Monmouth County Library, Eastern Branch, Route 35, Shrewsbury, NJ

The Public is Welcome – But Registration is Required

FREE DINNER

Registration & Directions   http://ewh.ieee.org/r1/njcoast/register.htm

ABSTRACT – We consider the problem of out-of-band quantization noise suppression in the general family of direct digital-to-RF up-conversion circuits, including digitally-segmented polar-modulated power amplifiers, or digital PA's (DPA). In such power amplifier architectures, the DPA is designed to have N parallel segments (or PA sub-sections), where N equals the number of bits representing the base-band amplitude component of the baseband IQ signal. The DPA segment gains are designed to follow a ''power-of-2'' weighting pattern. That is, the segments are weighted as 2n; n=0,...,( N-1). The outputs of the DPA segments are then RF-combined in a proper manner to result in an RF carrier that is amplitude-modulated by a quantized representation of the base-band amplitude signal. The digitally-segmented PA architecture faces an important challenge, which is how to reduce the output noise resulting from quantizing the base-band envelope signal. In this talk, we address such a problem by introducing a novel signal-processing solution, which we refer to as ''Segmented-Filtering (SF)''. In order to assess the capability of the proposed SF solution, we provide performance analysis and results that have been obtained via circuit-level computer simulations as well as laboratory measurements. Our proposed approach has demonstrated the ability to preserve the required signal quality and PA efficiency, while providing more than 35dB attenuation of the quantization noise. Hence eliminating the need for substantial post-PA pass-band RF filtering, which is known to be costly and inefficient.

SPEAKER’s BIO - (S’91-M’97-SM’00) received the B.S. degree in electrical engineering  (distinction with honor) from Ain Shams University, Cairo, Egypt, in 1991 and the Ph.D. degree in electrical and computer engineering from Queen’s University at Kingston, Ontario, Canada, in 1997. During 1991-1992 he was an Appointed Teacher and Laboratory Assistant at the Department of Communications and Electronics Engineering, Ain Shams University. During 1992-1997 he was a Research and Teaching Assistant at the Department of Electrical and Computer Engineering of Queen’s University at Kingston. While at Queen’s University, Dr. Ahmed has received numerous major scholarships and awards including the Canadian International Development Agency (CIDA) Scholarship, the Ontario Graduate Scholarship (OGS), the Queen’s University R. S. McLaughlin Fellowship and the Queen’s University Dean’s Award. Since 1997, Dr. Ahmed has been working in the telecom industry where he has held several senior technical and management positions at major industrial enterprises including Bell Northern Research (Nortel Technologies), Bell Laboratories (Lucent Technologies), M/A-COM (Tyco Electronics), Qualcomm Inc. and the Broadcom Corporation. He has been a recipient of numerous career awards including the M/A-COM, Tyco Electronics, Impact Award, the M/A-COM, Tyco Electronics, Key-Contributor Award and many patent awards from Lucent technologies, Tyco Electronics and Qualcomm Inc. Dr. Ahmed’s research interests and technical experience include information theoretic considerations for fading channels, coding and signal processing for fading channels, signal detection and estimation, wireless multiple-access techniques, transceiver design, military battlefield communication networks, and mobility and resource management in wireless networks. Dr. Ahmed holds 27 U.S. patents to-date and has more than 30 pending patents. He has also authored/co-authored more than 50 original research articles. Dr. Ahmed is a Senior Member of the IEEE. He is a Green-Belt Six-Sigma and has taught as an Adjunct Professor at the Stevens Institute of Technology and the New Jersey Institute of Technology. Dr. Ahmed has been listed multiple times in several of the Marquis “Who’s Who” Encyclopedias including “Who’s Who in America”, “Who’s Who in Science and Engineering”, “Who’s Who in World” and “Who’s Who in emerging Leaders”.

QUESTIONS CAN BE DIRECTED TO

DRU REYNOLDS, CHAIR, AEROSPACE AND ELECTRONIC SYSTEMS CHAIR AT DRU@REYNOLDSRECRUITERS.COM; or  PRAKASH KHANDURI, CHAIR, CIRCUIT AND SYSTEM / SIGNAL PROCESSING CHAPTER,  KHANDURI@BROADCOM.COM

OR TO WALID AHMED, WALIDMAIL@YAHOO.COM