Multi-granular Waveband Switching in Optical Networks

Dr. Xiaojun Cao

Rochester Institute of Technology

Abstract:

Optical network employing wavelength division multiplexing (WDM) is a promising solution to meet the high bandwidth requirements of emerging applications such as IPTV, VoIP, e-science and e-healthcare. The rapid advances in dense WDM technology with hundreds of wavelengths per fiber and world-wide fiber deployment have brought about a tremendous increase in the size (i.e. number of ports) of optical cross-connects, as well as in the cost and difficulty associated with controlling such large cross-connects. The talk will introduce a new switching paradigm called multi-granular waveband switching (WBS), which, in conjunction with new Multi-Granular Optical Cross-connects (or MG-OXCs), can significantly reduce the port count, associated control complexity, and cost of optical cross-connects. In particular, it is shown that WBS is different from traditional wavelength routing in terms of challenges such as MG-OXC architecture design, how to satisfy static (offline) traffic, how to accommodate dynamic (online) traffic, how to efficient utilize wavelength / waveband conversion, and how to provide protection/restoration. Then the talk focuses on one particular challenge, i.e., how to satisfy a set of static traffic with minimal number of ports in multi-granular switching network, which is shown to be an NP-Complete problem. To solve this, an integer linear programming model, efficient heuristic algorithms and numerical analysis are presented.

Biography:

Xiaojun Cao is an assistant professor in the College of Computing and Information Sciences at Rochester Institute of Technology. He received the B.S. degree in Engineering Physics from Tsinghua University, Beijing, China, in 1996, the M.S. degree in EE from Chinese Academy of Sciences in 1999, and the Ph.D. degree in Computer Science from The State University of New York at Buffalo in 2004. His research interests include modeling, analysis, and protocols/algorithms design for optical and wireless networks. Dr. Cao received the NSF CAREER award in 2006.