## Slide 1: HOW TO BE BETTER PREPARED FOR ESD TESTING
By Rick Candelas
Extron Electronics
October 25, 2016

## Slide 2: AGENDA
This presentation will focus on how to be better prepared ourselves for ESD testing.
Understand the standard.
Organizing a test plan.
Performing the Test
What do you do after the test?
Basic Troubleshooting

## Slide 3: STANDARD
  Read the standards yourself.
  Cant understand it if you haven’t read it.
  New to ESD, understanding the standard is extremely important.
  Sometimes you have to read it many times before you understand it.
Ask for help from a reliable test lab.
  Watching how a test lab performs the test and documents the data is a good way of learning how to do your own tests.

## Slide 4: STANDARD – Test Levels
IEC 61000-4-2 Test Levels |  | 
Level | Contact Discharge Test Voltage (kV) | Air Discharge Test Voltage (kV)
1 | 2 | 2
2 | 4 | 4
3 | 6 | 8
4 | 8 | 15
x | Special | Special
Note 1: Test can be performed at special levels (Ex. 1.5 times the product specific standard level). Note 2: Product specific standard determine what level to use. Depends on end use & installation environment. |  | 

## Slide 5: STANDARD – Test Levels
Each product specific standard lists details & actual test levels.
ITE - EN 55024 (Contact: 4kV, Air: 8kV)
  Testing at lower levels are not required for Contact discharges
Pro Audio/Video EN 55103-2 (Contact: 4kV, Air: 8kV except for E4 Contact: 2kV, Air: 4kV)
  E1: Residential (home use)
  E2: Commercial & light industrial (theaters, television studios)
  E3: Urban outdoors (stages)
  E4: Controlled EMC Environment (recording studio)
  E5: Heavy Industrial (close to broadcast transmitters)
Medical EN 60601-1-2 (Contact: 6kV, Air: 8kV)
  Test performed with the power at any one of its nominal input voltages and frequencies.

## Slide 6: TEST PLAN
Best to create a test plan in the early stages of the product.
Usually a test lab can assist with the test plan.
Used to make sure all the unit under test is ready prior to testing so that expensive lab time isn’t wasted.
Also to evaluate and understand test points that may cause the unit to fail or even worse be damaged.

## Slide 7: TEST PLAN – Items to Include
Product details
  Name, model, serial number and brief description.
Standard that will be tested to.
  Include revision & date
Test levels (as discussed earlier)
  Standard or special level

## Slide 8: TEST PLAN – Pass / Fail Criteria
Defined a performance criteria to determine PASS / FAIL.
Usually the criteria requires that a product operate as intended after the test.
  Self-recover without operator intervention.
  No degradation or loss of function is allowed below a performance level specified by the manufacturer.

## Slide 9: TEST PLAN – EUT Setup
Configure the EUT as close as possible to its typical use.
Include a Block diagram
Explain in further detail special arrangements.
List all support equipment (CE approved)
Cabling (shielded or non-shielded)
Table Top or Floor standing?

## Slide 10: TESTING – Test Equipment
Is the ESD generator the correct piece of equipment to perform the test?
  Verify waveform. Do you or the lab do this.
470kΩ bleeder cable
  Used to isolate the HCP from the ground ref plane. Verify before test.
Horizontal coupling plane size (1.6m x 0.8m)
Vertical coupling plane size (0.5m x 0.5 m)

## Slide 11: TESTING – Test Setup
Test Environment – Make sure to document this.
  Environmental conditions are extremely important for ESD.
  Temp: 15-35° C, Humidity: 30-60%, Pressure: 86-106kPa.
  These are typical office environments.
  Make sure you or the lab has the instrument to measure these parameters.

## Slide 12: TESTING – Test Setup
Test generator must be perpendicular to the surface of the EUT;
AIR discharge, tip must approach the EUT as fast as possible & touch the EUT;
CONTACT, tip must touch the EUT before the discharge switch is operated
Non-earthed apparatus –EUT must be discharged between each pulse, e.g. via bleed resistor
Number of discharges – Determine the amount of discharge.
  IEC 61000-4-2 says to do ten in each polarity at each point, 1 discharge/sec.
  EN 55024 says to do a minimum of 200 discharges

## Slide 13: TESTING – In House vs. Accredited Test Lab
    Limit cost with pre-compliance testing.
    Save a great deal of time, money, and headaches if ESD testing is done at all stages in a product’s development.
    Discover if there are any issues before a mass-produced item goes for final compliance testing.

## Slide 14: TESTING – Development
    Typically performed in-house in the prototype stage.
    Low-cost ESD checks
    Might be cost effective to purchase or rent a used ESD generator.
    Evaluate potential test points and problems.
  Ex. LCD screens are notorious for having ESD issues. Possible fix could be conductive film

## Slide 15: TESTING – Pre-Compliance
In-House or at a test lab
Product has finally come together in its intended enclosure.
  Check for over spray or Excess paint
  Grounding
Can be still be modified quickly and re-tested.
Design engineers should be present with the necessary equipment & components to do re-work in a hurry.

## Slide 16: TESTING – Final Compliance
      Performed at an accredited test lab.
More expensive per day and allows little to no disruption in the test.

## Slide 17: TESTING – Sustaining Compliance
If 1 sample tested passed, does it mean that every sample shipped will pass?
  Absolutely not. Unless there are proper procedures in place.
Procedure should include the following:
  Design to reduce large variability in manufacture due to different components, assemblies, or wiring.
  Control all changes, software bug fixes & upgrades
Sample test can be integrated into a production line to improve confidence (Ex. 8kV air discharge only)

## Slide 18: TESTING - THIRD PARTY LABS
    Know how you are getting billed.
    Test plan comes in very handy to ensure the test lab & the manufacturer are on the same page.

## Slide 19: TESTING - AUDIT THE LAB
Correct test equipment, procedures, standards, certificate & scope of accreditation.
Skilled engineer/technician or ESD troubleshooting expert.
Does the lab perform all the necessary verifications.
ESD generator calibrated?
How do they handle their equipment?
Watch them perform test

## Slide 20: TESTING – Completed
Hopefully passed.
Document everything
  Customer as well as the test lab
Setup pictures
Report (Accredited)
Test Sample. Keep it.

## Slide 21: BASIC TROUBLESHOOTING
Make sure you are not getting a false failure.
  Check cables and support equipment
Take spare samples – ESD can be destructive.
Take schematics / layout
Troubleshooting Kit with resistors, capacitors, TVS, etc.
Remove paint overspray between contact surfaces of metal enclosures.

## Slide 22: SUMMARY
Understanding the standard is critical.
The Test plan is your best friend.
Know where & how the test will be performed.
Get the proper documentation and save your golden sample for future reference.
Be prepared to troubleshoot.
Goal is not necessarily to get passing results but to get valid and repeatable results.

## Slide 23: REFERENCES
IEC 61000-4-2:2008 (identical to EN 61000-4-2:2009)
European Harmonized Standards - http://ec.europa.eu/growth/single-market/european-standards/harmonised-standards/
IHS - http://global.ihs.com/
BSI - http://shop.bsigroup.com/

## Slide 24: QUESTIONS?
rcandelas@extron.com