## Slide 1: A Current-Centric Approach for EMI Coupling Physics and Concepts in High-Speed Design
Jim Drewniak
Missouri S&T EMC Laboratory
Missouri-University of Science and Technology

## Slide 2: EMI Concepts and Physics: Module Overview
Reminders
  EMI problem at “30,000 feet”
  EMI coupling paths
A short laundry list of representative examples
A current-based paradigm for anticipating and diagnosing EMI coupling paths
  A physics-based paradigm for EMC design, diagnosis, mitigation
  Tracing current paths – intentional and un-intentional
    The basic physics through an example – current changing reference
    USB interface
    DVI interface
Developing models
The Maxwell Equations only – paradigm doesn’t apply
Managing currents

## Slide 3: EMI/RFI Problem Constituents
ideally a pair of terminals with well-defined V, & I – a port
COUPLING PATH
(transfer function
description ideal)
EMI ANTENNA
(or RFI victim)
SOURCE
V1
I1
V2
I2
ICs
  clocks
  address/data
  power supply
Signal/IO coupling
I/O transition thru power planes
Heatsink illumination
Traces crossing gaps
Line to connector I/O coupling
…
Cables
Apertures, slots & gaps, parallel plates
Ideally solve the problem here,
often on the PCB with layout
(lowest cost)
Locating ports for source and antenna that are closest to the coupling path geometry is essential for successful experimentation to determine the coupling path
LCD Clock-line
Port
FM-Tuner Port

## Slide 4: Divide and Conquer for EMI Diagnosis and Mitigation
3. Identify and characterize the transfer function for the coupling path;
Develop a SPICE model when possible
COUPLING PATH
(transfer function
description ideal)
V2
I2
V1
I1
ZA
EMI ANTENNA
GEOMETRY
2. Conducors, slots, or parallel plate edges
ZA
SPICE model from closed –form or full-wave numerical modeling
1. Identify the source from its spectrum

## Slide 5: Anatomy of the EMI Frequency Response
COUPLING PATH
EMI ANTENNA
SOURCE
V1
I1
V2
I2
a pair of terminals with well-defined V, & I – a port (only the case for a TEM wave or electrically small geometry)
|ZA (jw)|
I2
source
antenna
Careful with this formula

## Slide 6: EMI Concepts and Physics: Module Overview
Review
  EMI problem at “30,000 feet”
  EMI coupling paths
A short laundry list of representative examples
A current-based paradigm for anticipating and diagnosing EMI coupling paths
  A physics-based paradigm for EMC design, diagnosis, mitigation
  Tracing current paths – intentional and un-intentional
    The basic physics through an example – current changing reference
    USB interface
    DVI interface
Developing models
The Maxwell Equations only – paradigm doesn’t apply
Managing currents

## Slide 7: EMI Coupling Paths (discussed in this seminar)
Electrically “not”-small
1D Distributed transmission-line
Field coupling/illumination
on strip
on GND
Pigtail
Electrically small (lumped)
E-field/capacitance (displacement current)
H-field/inductance (conduction current)
Absorbing material for mitigation
Heatpipes running above PCB traces along the length

## Slide 8: Coupling to Heatsinks from Traces in Proximity
signal trace
PCB GND
heatsink
IC
Conduction current – carried by electrons
Displacement current – carried by time-changing E-field
on strip
on GND
The intentional signal current and its signal return current on the strip conductor and PCB GND signal return conductor
Q: There are two un-intended current paths. What are they?

## Slide 9: Coupling from Currents “Jumping” Signal Return References
Method: When signals transition layers, transition 2 layers to use the lower side of the GND reference plane upper side being used, or transition to another GND layer with a GND stitching via or multiple vias adjacent to the signal transition via.
10-15 dB EMI reduction with new “layout”
microcontroller
ASIC

## Slide 10: Coupling to Cables Draped across the Layout
Similar to heatpipes, any conductor, .for example cables draped across the layout can be coupled to with EM energy (1D wave coupling, E-field, or H-field) and radiate (or be part of a coupling path to other radiators)
Coupling from IC
1D distributed Coupling from circuit net
Q: When would 1D wave coupling be expected?
Q: E-field coupling?
Q: H-field coupling?
Coupling from IC

## Slide 11: Coupling from Traces Crossing Gaps in Signal Return Planes
EMI
CM-TL Currents on a Differential Signal Pair
on strips
on GND
Conduction current – carried by electrons
Displacement current – carried by time-changing E-field
Comments:
Single-ended – work to avoid a trace with high-speed or high-frequency (intended or un-intentional) crossing a gap in its signal return reference. (Note that for DDR the signal return reference is a PWR for the address, so that should be continuous beneath signal.) AC stitching across the gap with a closely spaced decoupling capacitor, or a carefully design balan across the gap can be used successfully if a good model including parasitics is developed and verified, but it is risky in general.
Differential – the CM-TL mode has the same non-net current on the reference plane as a single ended signal. It is worth working to avoid differential signal crossing gap too, and if done, best designed with good modeling in the process.

## Slide 12: Cable Connector Shell-to-PCB Connector Shell
  The Shell-Shell interface is only connected through 6 contact points (3 on top shown).

## Slide 13: 3D Wave Coupling – Radiation from High-Speed Connectors
radiation
GND
GND
GND
S+
S-
Circulation integrals give antenna currents
Total radiated power
EMI)
Q: What type of antenna is at this frequency?
Resonant length
Connector with Large PCB Plane
Middle pair

## Slide 14: 3D Wave Coupling – Coupling through Cavity Mode
2.4 GHz receive antenna at 1 cm distance
Dimensions (all approximate):
Enclosure (30cm x20 cm x 2.5 cm)
Loop 1.5 cm long x 0.5 cm high
Apertures (5 mm x 5 mm)
Small driven loop in enclosure at 2.4 GHz
end view
Coupling to propagating cavity mode
Evanescent wave leakage to Wi-Fi antenna
Antenna
Memory

## Slide 15: EMI Concepts and Physics: Module Overview
Review
  EMI problem at “30,000 feet”
  EMI coupling paths
A short laundry list of representative examples
A current-based paradigm for anticipating and diagnosing EMI coupling paths
  A physics-based paradigm for EMC design, diagnosis, mitigation
  Tracing current paths – intentional and un-intentional
    The basic physics through an example – current changing reference
    USB interface
    DVI interface
Developing models
The Maxwell Equations only – paradigm doesn’t apply
Managing currents

## Slide 16: Physics-Based Models and Methodology for EMI
Geometry (and Materials)
Model – mixed SPICE(network), TL, Full-Wave
Trace all current paths
  conduction – L/H-field
  displacement – C/E-field
Identify nodes/ports with well-defined V, I (check with full-wave)
Geometry features and nodes/circuit elements must have direct correspondence
Response and circuit model correspond
Response (Time Domain – Frequency Domain)
Response and geometry features correspond
Circuit Model
S- Parameters
(or Z-parameters)
EMI ANTENNA
SOURCE
V1
I1
V2
I2
engineering path
physics
trial-and-error path
Ports are required in this concept

## Slide 17: Current Paths at High Frequency
Current physics
  Conduction current
  Displacement current
  Skin depth and consequences for current paths
Current flows in loops (conservation of charge)
Intentional currents
  Single-ended – TL currents
  Differential (differential-mode TL, common-mode TL currents)
Unintentional antenna currents
  Cables – shielded, un-shielded
  Antenna currents on board-to-board connectors of resonant dimensions
  Slots, gaps, apertures
Un-intentional currents in EMI coupling paths
+
-
Signal
GND
on strip
on GND

## Slide 18: Conduction and Displacement Current – TL
load
Source
(unit step in time, 0-to-1 transition)
Ic
(conduction current
carried by e-)
Ic
+
Id
(displacement
carried by time-changing electric field)
location of
wavefront
voltage wave
v(x,t)
-
(current reference direction)
current wave i(x,t)
signal current
return conductor
i(x,t), v(x,t) = 0 ahead
of the wavefront
signal current
conductor
Conduction current is DC behind the wave front
Q: If the current is zero in front of the wave-front, how can there be a DC (conduction) current in one direction on the signal conductor, and in the opposite direction on the signal return?
Electrons are very athletic and they jump from the signal to return conductors.
A second type of current is displacement current, and the current continuity is maintained by the displacement current at the wave-front where there is a time-changing E-field (voltage for TEM wave).
Microstrip example
signal current conductor
signal return currentconductor
(conduction current
carried by e-)

## Slide 19: Skin Effect and Skin Depth
And replace the exponential volume distribution of current with a uniform distribution of depth in the conductor
And consider the E- and H-fields beyond one skin depth to be negligible
(good conductor)
A uniform plane wave (UPW) is such that constant magnitude and constant phase fronts are planar.
z
x
J(x) – the real current in the conductor
RGW UPW
free space
good conductor
E- and H-fields decay away rapidly in good conductor

## Slide 20: Skin Depth for Copper
ds=2.08 mm
ds=0.66 mm
ds=6.6 mm
ds=20.8 mm
ds=66 mm
ds=209 mm
1 oz. Cu = 35 mm
0.5 oz. Cu = 17.5 mm
For typical high-speed PCB nets, all conductors have 2 surfaces on which current flows and no fields in the interior of the conductor.
1 oz Cu = 5d at 100 MHz

## Slide 21: Skin Depth and Current at High-Frequency
Q: Which is the correct current path? Assume the signal is such that the spectrum is such that the copper thickness is several skin depths thick.
+
-
Signal
GND
(a)
+
-
Signal
GND
(b)

## Slide 22: Skin Depth and Current at High-Frequency
Q: What are the correct physics for the (correct) current path below?
+
-
Signal
GND
The current must return as shown because of skin depth.
The current takes the path of least impedance and this is the lowest impedance path.
At high frequencies, when the copper planes/area fills that function as the signal reference conductors are several skin depths thick, no E or H fields can exist inside these planes. In order for this to be the case, currents have to “see” a partner and cannot “look through” conductors.

## Slide 23: Current Flows in Loops
on strip
on GND
Current flows in loops (no charge collecting), and if there is a source in current loop or path, then current will return to the source.
Microstrip current
signal current conductor
signal return currentconductor
(conduction current
carried by e-)
signal trace
PCB GND
Heatsink (grounded in 1 place)
IC
Electrically short is capacitance
Electrically short is inductance
Note that high-frequencies are considered here so that the current flows on conductor surfaces.
Trace all current paths
intentional – signal
Un-intentional – due to parasitic coupling and can lead to EMI
Q: The heatsink is grounded, why is there still a displacement current between the heatsink and the PCB GND shown as part of the return path of the in-intended current coupled to the heatsink?
Conduction current – carried by electrons
Displacement current – carried by time-
changing E-field
Antenna conduction current
EMI

## Slide 24: Intentional Currents – TL Signal Currents
There are currents on ref. plane but the net current on reference plane
There is net current on the reference plane
Transmission-line (TL) currents for a single-ended signal:
Odd-Mode
Transmission-line differential mode (DM-TL)
Even-Mode
Transmission-line “common”-mode (CM-TL)
V
+
-
Transmission-line (TL) currents for a differential signal pair:
V
+
-
i
d1
i
ireturn
V
+
-
symmetry plane
d1
+ V
+
-
+ i
- i
-V
+
-
anti-symmetry plane
+ + + + + + +
- - - - - -
-
-
EMC people sometimes refer to intentional single ended currents as “differential”-mode currents, and any un-intentional currents, on heatsinks, anywhere in the PCB design, on cables, etc., as “common”-mode currents. It is worth avoiding using the same name for different physics.

## Slide 25: Un-intentional EMI “Antenna” Currents – Shielded Cable
The current on the outer surface of the cable shield is often denoted “common-mode” current. It is a radiating current and denoted here as an antenna-mode current.
There is a third wire in the 3-conductor system that is attached to PCB GND, and this is the return for the CM-TL currents.
Not a perfect 360o connection of shield braid to metal shell
Q: What is the impact of the imperfect shield connection? How can this be quantified – measured, modeled, or calculated?
Q: What are mitigation approaches? How to choose?
Notes: Q

## Slide 26: Un-intentional EMI “Antenna” Currents – Un-shielded Cable
Antenna currents (conductions) go down all conductors and “return” by displacement current to the outer surface of the metal enclosure wall. (These currents are often call “common-mode” currents. Bad choice of words.)
The single-ended signal currents are sometimes denoted “differential-mode” currents. (Bad use of these words.)

## Slide 27: Un-intentional Currents across/around Slots
CM-TL Currents on a Differential Signal Pair
on strips
on GND
Conduction current – carried by electrons
Displacement current – carried by time-changing E-field

## Slide 28: Un-intentional Antenna Currents on Heatsinks
Conduction current – carried by electrons
Displacement current – carried by time-changing E-field
heatsink
IC
Radiation
(cavity mode)
Radiation
(dipole mode)

## Slide 29: Intentional and Un-Intentional Currents on PCBs
signal trace
PCB GND
heatsink
IC
Conduction current – carried by electrons
Displacement current – carried by time-changing E-field
on strip
on GND
The intentional signal current and its signal return current on the strip conductor and PCB GND signal return conductor
Q: There are two un-intended current paths. What are they?

## Slide 30: EMI Concepts and Physics: Module Overview
Review
  EMI problem at “30,000 feet”
  EMI coupling paths
A short laundry list of representative examples
A current-based paradigm for anticipating and diagnosing EMI coupling paths
  A physics-based paradigm for EMC design, diagnosis, mitigation
  Tracing current paths – intentional and un-intentional
    The basic physics through an example – current changing reference
    USB interface
    DVI interface
Developing models
The Maxwell Equations only – paradigm doesn’t apply
Managing currents

## Slide 31: USB Cable/Connector/Enclosure/PCB Interface
Pigtail

## Slide 32: DVI Connector Geometry
GND
Tx-
Tx+

## Slide 33: EMI “Antenna” Currents on Cable
PCB GND
Connector shell to PCB GND
Notes: Q

## Slide 34: Cable Shield to Connector Shell
Not a perfect 360o connection of shield braid to metal shell

## Slide 35: Cable Connector Shell-to-PCB Connector Shell
  The Shell-Shell interface is only connected through 6 contact points (3 on top shown).

## Slide 36: PCB Connector Shell-to-Enclosure
Two screws connector shell to enclosure

## Slide 37: PCB Connector Shell-to-PCB GND
Three “dimples” connector shell upper for PCB GND
Connector shell to PCB GND
PCB GND

## Slide 38: EMI Concepts and Physics: Module Overview
Review
  EMI problem at “30,000 feet”
  EMI coupling paths
A short laundry list of representative examples
A current-based paradigm for anticipating and diagnosing EMI coupling paths
  A physics-based paradigm for EMC design, diagnosis, mitigation
  Tracing current paths – intentional and un-intentional
    The basic physics through an example – current changing reference
    USB interface
    DVI interface
Developing models
The Maxwell Equations only – paradigm doesn’t apply
Managing currents

## Slide 39: Modeling for Engineering Methodology and Calculations
signal trace
PCB GND
heatsink
IC
The intentional signal current and its signal return current on the strip conductor and PCB GND signal return conductor
Conduction current – carried by electrons
Displacement current – carried by time-
changing E-field
Antenna conduction current
signal current on strip
signal return current on GND
Un-Grounded Heatsink Geometry

## Slide 40: Engineering Methodology and Calculations – Coupling Path
Assume the coupling path is capacitive? (What are the physics underlying this assumption?)
signal current on strip
signal return current on GND
Q: What should be the spacing s between a high-speed trace and a heatsink?
IC
Conduction current – carried by electrons
Displacement current – carried by time-
changing E-field
Antenna conduction current
EMI

## Slide 41: Modeling for Engineering Modeling Methodology– Decomposition
Q: What should be the spacing s between a high-speed trace and a heatsink?
Strategy: “Divide-and-Conquer”
Break coupling path into pieces
Aggressor source (data rate, trise, tfall)
Aggressor TL sections (coupled)
Aggressor TL – heatsink coupling
Radiation calculations
Shielding calculations
source
data rate, trise, tfall

## Slide 42: Engineering Modeling Methodology– Model Development
Develop a model for this piece
Assume the coupling path is capacitive? (What are the physics underlying this assumption?)
Q: What should be the spacing s between a high-speed trace and a heatsink?
IC
ePCB
er
Coupled TL model
Q: How to approximate tHS and wHS in the equivalent MTL model?
Q: Can the geometry for Ccoupling be normalized so that the coupling scales with geometry?

## Slide 43: Modeling Methodology – Model Assembly and Calculations
Q: What should be the spacing s between a high-speed trace and a heatsink?
source
data rate, trise, tfall
|ZA (jw)|
IA
|ZA (jw)|
Determine ZA from microstrip patch antenna
|ZA (jw)|

## Slide 44: Conclusion
Understanding and identifying un-intentional current paths is a helpful supplement to experienced EMC design “best practices” that can aid in:
Anticipating EMI coupling paths
Diagnosing EMI coupling paths through measurements and experiments
Mitigating EMI problems
And in some cases quantifying EMI problems