## Slide 1: Plugged Into the Matrix The North American Power Grid: Past, Present and Future
Paul M. Grant
Principal, W2AGZ Technologies
Visiting Scholar, Stanford (2005-2008)
EPRI Science Fellow (retired)
IBM Research Staff Member Emeritus
w2agz@w2agz.com
www.w2agz.com
IEEE OEB Life Member Meeting
18 April 2018
Livermore, CA

## Slide 2
To
Electric Power Delivered
From Electrons Paired
…And… Back
Again
?
-- A Personal Journey in Applied Physics --
-- IBM, EPRI, and Beyond --
Paul M. Grant
IBM (1953-1993)
Joined 1953 (age 17)
SAGE/NORAD (MIT)
Clarkson/Harvard
Magneto-optics
Displays/Printers
Organic Conductors
DFT
Superconductivity
High-Tc
Sabbatical (UNAM)
EPRI (1993-2005)
High-Tc Power Apps
Wide Bandgap SCs
Power Electronics
“Hot” Fusion
“Smart Grid”
“SuperGrid”
“Climate Change”
Visionary Energy Societies
W2AGZ (2005-?)
Due Diligence
Tet-CuO (Stanford)
“Proxy” DFT
RTSC via DFT
IASS Potsdam
Dual Use of NG Pipeline ROWs for Co-transport of Electricity via HTSC Cables (e.g., Keystone)

## Slide 3: …in their shoes…
Paul Archibald Grant
  W2AGZ
  US Navy, WWII
  IBM, 1948-1974
  Ski Patrol, 1948-1970
Mary Ann Whalen Grant
  CYO BB Champ, 1921
  NYS Bowling Champ, 1939
  Women’s Baseball, ‘33-’47
  CHG&E, 1927-1965

## Slide 4: IBM Poughkeepsie - 1952
Visit www.w2agz.com for the whole story

## Slide 5: 1953 Project Sage – IBM/MIT
My Teenage Toy!

## Slide 6
Eta Kappa Nu, ‘60

## Slide 7
My Senior Thesis Morphed
Into the GMR Read Head
Employed in Hard Drives

## Slide 8: My Virtual Grandfather (@ 94)

## Slide 9: US Electric Power 101

## Slide 10: Electricity Today - The Crown Jewel of the US Economy
§
~$2 trillion total asset value
§
$344 billion annual revenues
§
142 million customers
§
3273 utilities
Without electric power the $14.3 trillion
U.S. economy would come to a halt

## Slide 11: NYC circa 1890s

## Slide 12: The US Electrical System

## Slide 13: The US Transmission Grid(s)
300,000 km
500 companies
10% Losses

## Slide 14: North American HVDC

## Slide 15: Pacific Intertie
HVDC, +/- 500 kV, 3.1 kA, 3.1 GW
1,362 km
~50% of LA Power Consumption
Converter/Inverter Losses ~ 5%
Ohmic Losses ~ 10%
Celilo I/C Station
“A Mountain of Silicon”

## Slide 16: NERC Interconnects
Source: DOE 2006 National Electric Transmission Study

## Slide 17: The Grid: A Journey Though the Heart of Our Electrified World
By Phillip F. Schewe
Joseph Henry Press, 2007 (Buy It!)
Reviewed by Paul M. Grant:
Plugged into the matrix
The rise and potential fall of the US electricity grid
Nature 447, 145 (2007)
http://www.w2agz.com/Publications/Book%20Reviews/06%20%282007%29%20Plugged%20Into%20the%20Matrix.pdf

## Slide 18: Superconductivity 101

## Slide 19: Models of Electrical Conductivity
The Most Popular:
R
T
Freezes Out!
e-

## Slide 20: Models of Electrical Conductivity
Reality:
R
T
Limited by
Impurities!

•
e-

## Slide 21: 1911 A Big Surprise!
Thus the mercury at 4.2 K has entered a new state, which, owing to its particular electrical properties, can be called the state of superconductivity
Gilles Holst, H. Kamerlingh-Onnes (1911)

## Slide 22: Physics of Superconductivity (1957 – 2006)
+
+
+
+
•
e-
•
e-
Electrons Pair Off!
BCS Equation

## Slide 23: It takes two to Tango
Notes: Ney Mello, 9/11 survivor decided to leave his career as investment banker and turn to tango

## Slide 24: conductor

## Slide 25: Semiconductor

## Slide 26: SUPERCONDUCTOR

## Slide 27: Important Numbers in Superconductivity
Transition Temperature, TC Way below 300 K
Critical Current Density, JC 10-2 - 106 A/cm2
Critical Magnetic Field, HC 10-4 - 10 T
London Penetration Depth,  10 - >1000 Å
Pippard Coherence Length,  10 - >1000 Å
G-L Parameter,  = / 0.01 - 100
NB! All these numbers depend on each
other. E.g., HC ~  

## Slide 28: TC vs. Year: 1911 - 1980
Year
0
5
10
15
20
25
1900
1910
1920
1930
1940
1950
1960
1970
1980
Temperature (K)
Hg
Pb
NbN
V3Si
Nb3Sn
Nb3Ge
Cubic Metals

## Slide 29: Properties

## Slide 30: MRI & “Big Physics”
Magnetic Resonance Imaging
Philips
Tevatron
Fermi National Laboratory

## Slide 31: 1986 Another Big Surprise!
Bednorz and Mueller
IBM Zuerich, 1986
Onset TC = 40 K !

## Slide 32: 1987 “The Prize!”

## Slide 33: March 3, 1987 “123” Discovered

## Slide 34: Woodstock of Physics NYC, 1987
Physicists’ Night Out!

## Slide 35: “The Great Communicator”
Notes: 35

## Slide 36: Today
Year
Tc (K)

## Slide 37: Where Can We Apply Superconductivity to Electric Power?
Potentially Everywhere
Notes: 37

## Slide 38: Gen II Coated Conductor
American Superconductor
SuperPower

## Slide 39: HTSC SuperCables: Brief History
EPRI SCDC
100 kV, 100 kA, 10 GW
Sumitomo 66 kV 3-in-1
Furakawa, 275 kV, 3 kA
St. Petersburg, Russia
~ 1997
~ 2014

## Slide 40: Pacific Intertie
HVDC, +/- 500 kV, 3.1 kA, 3.1 GW
1,362 km
~50% of LA Power Consumption
T&D Losses ~ 10%
Tear down the PI and replace with HTSC underground cables to capture this saving?
Ain’t gonna happen, baby!
Not a “compelling need!”
Even should the cost of the wire be zero!

## Slide 41: Required Reading! (Thanks to Steve Eckroad, EPRI)
Two EPRI Reports (available free from epri.com or w2agz.com)
  (2012) Superconducting Power Equipment; Technology Watch 2012 (1024190)
  (2013) SIU: Superconductivity for PDA (03002001)
Bottom Lines:
  Work continues on wire improvement and power application demonstration, although not at the pace of a decade ago.
  HTSC materials performance and costs have matured.
  What’s needed is a strong business case for HTSC power applications.
  Does there exist a “compelling need,” now or in the next decade, to effect a major and continuing deployment of HTSC in the electricity enterprise?

## Slide 42: “The Short Story”
Following the 1911 discovery, Kamerlingh Onnes attempted the construction of an electromagnet...unsuccessfully.
Throughout the second half of the 20th Century and up to the present, many successful demonstrations of superconducting cables, transformers, current limiters, storage units, rotating machinery, etc., have been carried out. Yet, to date, no significant markets (> 108 USD/yr) have emerged for deployment worldwide in the Electricity Enterprise.
  For a 1997 review, see “Superconductivity and Electric Power: Promises, Promises...Past, Present and Future,” P. M. Grant, IEEE Trans. Appl. Supercon. 7, 112 (1997). Available on request from www.w2agz.com.
  Today, the principal “power” applications of superconductivity remain cabling and deflection magnets for hadron colliders and solenoids for medical MRI.
As of today, all US HTSC power app demos have been concluded or are “on hold.”
What might constitute a “Longer Story?”
  Advancing a current “technology addiction.”
  Satisfying a compelling social need.
  Identifying a new opportunity.

## Slide 43: Energy Fraternal Twins

## Slide 44: However, we do indeed have a “compelling new opportunity!”
P.M. Grant, EPRI, 1998
...& hydraulic fracturing , aka “fracking”

## Slide 45: Natural Gas & Electricity
Chart: 
| Coal | Natural Gas | Nuclear | Hydroelectric | Renewables | Other
2012 | 0.38407 | 0.31155 | 0.19475 | 0.070003 | 0.055384 | 0.010612
2012 USA Electricity Generation by Primary Fuel Source
Wow!
“Fraternal Twins,”
Smart Grid News
16 April 2013

## Slide 46: The “Dual Use” Concept Embodied
Almost all NG used for electricity generation is “combusted” at a “local” delivery point using modern, efficient, combined cycle gas turbine (CCGT) technology.
Why not “combust” that gas portion so-used at the “well-head” instead and deliver the “electrons” over a low-loss HTSC dc cable? As well as reducing volume...and...frictional loss due to NG transported by pipeline.
...and...consider “recycling” well-head generated CO2 emissions into alcohols...and “pipe” those down the same ROW!
The ROW Dual Use concept has been documented in several peer reviewed journals as well as member magazines of the APS, IOP, IEEE, and Nature...contact the author/speaker for a linkable anthology.

## Slide 47: Does “Keystone XL” Provide a “Compelling Opportunity” to “Raise Our Fraternal Twins?”
Let’s encourage DOE to enlist EPRI, GTI, EIPC, INGAA,...in a collaboration to conduct an “engineering economy” study focused on the dual-use ROW concept.

## Slide 48
...and in the long term...
Electricity Conversion Assumptions
Wellhead Power Capacity | 18 GW (HHV)
Fraction Making Electricity | 33%
Thermal Power Consumed | 6 GW (HHV)
Left to Transmit as LNG | 12 GW (HHV)
CCGT Efficiency | 60%
Electricity Output | 3.6 GW (+/- 18 kV, 100 kA)
“Cryodelivery Systems for the Cotransmission of Chemical and Electric Power,”
P.M. Grant, AIP Conf. Proc. 823, 291 (2006).

## Slide 49
o Wroclaw
The Wola Obszańska (Lublin) gas field in Poland/Ukraine was discovered in 1989. It began production in 1992 and produces natural gas. The total proven reserves of the Wola Obszańska gas field are around 37 billion cubic feet (1×109m³). “Dual-Pipe” to Berlin?
Let’s Not Forget Europe!

## Slide 50: 2100: The World Runs Out of CH4
The Dual Use ROWs Remain
Replace the CCGTs with 1-2 GW Nukes
Use Half the Power to Electrolyze (Frack) Nearby H2O Reserves to Release H2 ,
Then Liquify and Use to Refridgerate Upgraded HTSC Cables (If Necessary!)

## Slide 51: The Energy SuperGrid

## Slide 52
http://w2agz.com/PMG%20SuperGrid%20Home.htm

## Slide 53
Published in
SCIENTIFIC AMERICAN
July, 2006
“System Crash”
Omni Productions, Vancouver, BC CBC Broadcast October, 2008
Notes: 53

## Slide 54: Exascale Energy for Our Great-Great GrandKids!
SuperCity
SuperSuburb
SuperGrid
SuperTrain

## Slide 55: “The Only Commercial Application of HTSC”
Now it’s graphene!

## Slide 56: A Model For the Future

## Slide 57: “A Thread Across the Ocean”
“The Story of the Trans-Atlantic Cable (1854 – 1866)”
John Steele Gordon
Cyrus Field American Capitalist
Isambard Kingdom Brunel English Engineer
William Thomson Irish Physicist

## Slide 58: What Kept Them Going?
The investors knew, that if communications with Europe could be cut from 2 weeks to 2 minutes, they’d all get…
FILTHY RICH!
  Estimates are that the total cost of the project in 2005 dollars was $100 M
  First year 1867 revenue in 2005 dollars as $10 M !

## Slide 59: The After-Story
1870
1903
The First Links in the World Wide Web!

## Slide 60: The Economic (Venn)Troika That Drives and Exploits Technology Innovation
Entrepreneurial Create the Economy “stuff” “jobs”
Societal Sustain the Economy “enlightenment” “infrastructure”
Governmental Protect the Economy “agencies” “military”

## Slide 61: Finale

## Slide 62: Superconductors - The Long Road Ahead – Foner & Orlando (1988)
“Widespread use of these [high temperature] superconducting technologies will have far more to do with questions of public policy and economics than with the nature of the new materials.”

## Slide 63: “You can’t always get what you want…”

## Slide 64: “…you get what you need!”