## Slide 1: Power Integrity for High-Speed Design on Multi-Layer PCBs Concepts and Physics
James L. Drewniak
Clear Signal Solutions and
Missouri S&T EMC Laboratory
james.drewniak@clearsig.com

## Slide 2: Contributors
IBM – B. Archambeault, S. Connor, M. Cocchini, W. Becker, M. Cracraft, A. Ruehli
Cisco – B. Achkir, S. Scearce, Q. Gaumer, M. Sapazhnikov
Missouri S&T – B. Zhao, S. Bai, S. Liang, X. Zhu, K. Shringapure, S. Pan, J. Xu, J. Fan

## Slide 3: PI Module Overview Part 1 – Concepts and Physics
The PDN problem
Noise on the PDN and an FPGA example
PDN design considerations
A couple of preliminary concepts
Current and inductance physics
A reduced order circuit model from a first principles formulation
Characteristic ZPDN and relationship to physics
Understanding PDN physics and design through examples
Identifying limiting physics in design
Adding decoupling capacitors

## Slide 4: PDN Problem
High-speed, integrated, and mixed electronic system
IC Die
PKG
VRM
Jitter
Decap
3D IC
Effect of PDN noise on I/O jitter
IC EMI source model?
Power Distribution Network
Power Distribution Network
VRM
Decoupling capacitors
Power net area fills

## Slide 5: Logic Transitions and Current Draw
switch
IC load
IC
driver
VDC
GND
CL
VCC
Z0, vp
GND
IC load
IC
driver
VCC
VCC
charge
LO to HI
Z0, vp
shoot-thru current
IC load
IC
driver
GND
VCC
0 V
discharge
HI to LO
Z0, vp
shoot-thru current
Shoot-thru current (and everything else we can’t account for)
Load charging current
Load discharge current
This charge to support IC switching must be provided by the PDN – package, PCB

## Slide 6: Voltage Switching/Dynamic Current Draw Disturbances
Dynamic current on power net causes disturbance and can lead to faulty switching, a source of jitter, and trouble in general
1
0
T1 and T2 are not simultaneous
GND
IC load
IC
driver
VPWR
VCC
charging current
VPWR+VNoise
shoot thru current
a trouble-maker
T1
T2
vL
ist
ilogic
iIC
banks of transistors for the PMOS and NMOS not perfectly synchronized

## Slide 7: PCB for FPGA Core PDN Noise Example
SMT capacitor pads for 0805, 0603, 0403
Power Supply BNC connectors (sensing line)
Bulk Capacitor
VCC SMA connector
FPGA dedicated clock input SMA U33
Power planes: VCC, VCCN, VCCPD
FR4 dielectric
Signal layers
Ground planes
Port 1
Port 2
Port 2 is beneath the FPGA package coax probe

## Slide 8: Current Draw and the Logic Waveform
FPGA core power only

## Slide 9: Dynamic Current Profile (calculated)
Rising clock edge
Reconstructed time domain current for a large number of toggle flip-flops
Falling clock edge
Logic toggles
FPGA Core power only

## Slide 10: Transient Current Waveform - Simulated
FPGA with 18% grey-code counters implemented

## Slide 11: Voltage Disturbance Calculations with Z-Parameters
V2
I2
(from IC simulation)
Spectrum Analyzer, Scope, other IC
V1
I1
ZL = 50 Ω
I2 is from IC simulation. Z21 and Z11 are both from impedance simulation (also are calculated from S-parameters from modeling or measurement).
PCB + (Package + On-die capacitance)
Then the PDN
noise voltage is
For measurement
otherwise
or impedance into another IC
PDN impedance IC sees for usual case

## Slide 12: PDN Noise Voltage Spectrum Prediction
|IIC(jw)|=|I2(jw)|
(source)
x
=
|VPDNnoise(jw)|=|V1(jw)|
Un-freindly things happen at resonances – lumped or distributed
BGA package & IC
|Ztransfer-PDN(jw)|
=|Z12(jw)|

## Slide 13: PDN Noise Voltage from Impedance
IIC(jw)
(source)
x
|Ztransfer-PDN(jw)|
=|Z12(jw)|

## Slide 14: Transient PDN Noise Voltage
NO De-Caps
WITH 16 De-Caps
The estimated and measured noise voltage were compared, with a 100 MHz clock input, multi-frequency FPGA configuration, on the bare board and decoupled board.
Inverse Fourier Transform to get
30 mV
15 mV

## Slide 15: PI Module Overview Part 1 – Concepts and Physics
The PDN problem
Noise on the PDN and an FPGA example
PDN design considerations
A couple of preliminary concepts
Current and inductance physics
A reduced order circuit model from a first principles formulation
Characteristic ZPDN and relationship to physics
Understanding PDN physics and design through examples
Identifying limiting physics in design
Adding decoupling capacitors

## Slide 16: PCB PDN Design Considerations
2a. Decoupling capacitors
top
bottom,
beneath IC?
IC
IC pins
Decaps
Power net area fill
location in stack
spacing to power return plane
total area fill
special materials
Effect of other ground/reference planes?
PWR
GND
2b. Decoupling capacitor connection -
PWR/GND via geometry
Package size
2c. Decoupling capacitor layout
How close to IC?
Shape – ring IC, on one side?
doublet
2a. Decoupling capacitors
value(s)
number (total C)
3. IC PWR/GND
Number pins
pin pattern
Pitch
on-package decaps

## Slide 17: PI Module Overview Part 1 – Concepts and Physics
The PDN problem
Noise on the PDN and an FPGA example
PDN design considerations
A couple of preliminary concepts
  Responses for RLC circuits
  High-frequency current path

## Slide 18: Reminder – Circuit Model Behavior with Frequency
Series
resonance
Parallel
resonance

## Slide 19: Reminder: Current Behavior
Conduction current – carried by electrons
Displacement current – carried by
+
-
Signal
GND
impeded by
admitted by
Current on a microstrip line for high-speed data
At high frequencies, when the copper planes/area fills that function as the signal reference conductors are several skin depths thick, no E or H fields can exist inside these planes. In order for this to be the case, currents have to “see” a partner and cannot “look through” conductors.

## Slide 20: PI Module Overview Part 1 – Concepts and Physics
The PDN problem
Noise on the PDN and an FPGA example
PDN design considerations
A couple of preliminary concepts
Current and inductance physics
  Conduction current path through layers (vertical) on PCB PDN and associated inductance
  Decomposing the inductance into pieces
  Current path across the power net area fill and the ground power return current

## Slide 21: The Objective and Guiding Physics: Conduction Current Path results in Inductance
Bottom decoupling capacitors
IC
GND
GND
GND
GND
GND
GND
GND
GND
GND
GND
PWR
IC
Top decoupling capacitors
Looking from the IC
Decoupling capacitors sharing IC vias
Notes: One inductor per via per cavity
MUTUAL TERMS
Rearrange – reduce is series.
Series
Parallel

## Slide 22: The Objective and Guiding Physics: Conduction Current Path results in Inductance
Bottom decoupling capacitors
IC
GND
GND
GND
GND
GND
GND
GND
GND
GND
GND
PWR
IC
Top decoupling capacitors
Looking from the IC
Decoupling capacitors sharing IC vias
Notes: One inductor per via per cavity
MUTUAL TERMS
Rearrange – reduce is series.
Series
Parallel

## Slide 23: The Objective and Guiding Physics: Condution Current Path results in Inductance
IC
GND
GND
GND
GND
GND
GND
GND
GND
GND
GND
PWR
IC
Top decoupling capacitors
Looking from the IC
Decoupling capacitors sharing IC vias
Bottom decoupling capacitors
Notes: One inductor per via per cavity
MUTUAL TERMS
Rearrange – reduce is series.
Series
Parallel

## Slide 24: Key Point – Current Path and Inductance
IC
GND
GND
GND
GND
GND
GND
GND
GND
GND
GND
PWR
IC
Top decoupling capacitors
Looking from the IC
Decoupling capacitors sharing IC vias
Bottom decoupling capacitors
pkg-to-PWR net area fill
caps-to-PWR net area fill
in PWR net area fill
Four contributions (current path pieces) to the ZPDN inductance
Above PCB to decaps
Notes: One inductor per via per cavity
MUTUAL TERMS
Rearrange – reduce is series.
Series
Parallel

## Slide 25: Geometry and Inductance Decomposition
GND1
GND2
GND3
GND4
GND5
GND6
PWR
Silicon Die
LPCB_IC
Labove
Labove
LPCB_Decap
LPCB_Decap
LPCB_Decap
LPCB_Plane
Labove
Must account for mutual L
Must account for mutual L
Must account for mutual L

## Slide 26: Current Path, and Inductance
Current path from IC to decaps in the power net area fill layer is better to be in line (and not cross cutouts, around corners, etc.). LPCB_plane is increased otherwise.
Notes: The real board geometry is shown on top. The model and response are shown at bottom right and left respectively. The response for increasing number of capacitors is compared at the bottom left. As number of capacitors increase, the capacitance at low frequency increases as a direct result. Also LEQ , converges into LIC as the capacitors are added. Thus, if LIC is lower, then the LEQ will converge to a lower value. LIC is independent of the capacitors placed on the PCB.

## Slide 27: Key Points
Production printed circuit boards that use area fills for the power net will have from 4 to over 40 layers. The IC package may have tens to hundreds of vias, and there may be tens to hundreds of decoupling capacitors. The complexity is high, but the current path physics are very straight-forward, though there will be many parallel paths.
The inductance associated with a current path can be decomposed into four pieces along the path.
Direct, “line-of-sight” current paths between the IC and the decaps will have less LPCB Plane inductance than current paths that cross cutouts, slots, go around corners, etc.

## Slide 28: PI Module Overview Part 1 – Concepts and Physics
The PDN problem
Noise on the PDN and an FPGA example
PDN design considerations
A couple of preliminary concepts
Current and inductance physics
A reduced order circuit model from a first principles formulation
  Impedance from a Maxwell’s equation formulation
  A many element physics-based model to a reduced order impedance equivalent circuit with inductance related to geometry decomposition

## Slide 29: Calculating Inductance from Current Path Physics
All current segments in all layers are modeled (often many thousands or tens of thousands) and self inductances for every segment and mutual between segments are extracted using the (first principles) cavity model.
Self and mutual inductances are included.

## Slide 30: Circuit Model for PCB PDN
physics-based circuit model
GND1
GND3
PWR
GND4
GND6
GND1
PIC_G1
GND3
+
-
-
+
PIC_G2
GND4
GND6
PWR
LPCB_Plane
LPCB_IC
LPCB_Decap
LPCB_Decap
LPCB_Decap
Labove
Labove
Labove
Labove
Labove
Labove
Labove
LPCB_IC
LPCB_Decap
LPCB_Decap
LPCB_Decap
LPCB_Plane
Ri
LPCB_IC
LPCB_Decap_i
Labove_i
G
Cdecap_i
CPlane
…
LPCB_Plane
All current segments in all layers are modeled (often many thousands or tens of thousands) and self inductances for every segment and mutual between segments are extracted using the (first principles) cavity model and a SPICE model is assembled.
Circuit reduction is used to get an impedance equivalent circuit model that coincides with the large-scale current path from IC package to decaps. Inductances are related to the current path on the geometry.

## Slide 31: Impedance Equivalent Circuit
GND1
GND2
GND3
GND4
GND5
GND6
PWR
Decaps on Bottom Layer
Decaps on Top layer
PKG + IC
Cdecap2
Cdecap1
Labove1
LPCB_Plane
Labove2
Cplane2
Cplane1
LPCB_Decap
LPCB_Decap
Includes mutual inductances

## Slide 32: Geometry and Impedance Equivalent Circuit
Ri
LPCB_IC
LPCB_Decap_i
Labove_i
G
Cdecap_i
CPlane
…
LPCB_Plane

## Slide 33: Key Points
All current segments in all layers are modeled (often many thousands or tens of thousands) and self inductances for every segment and mutual inductance between segments are extracted using the (first principles) cavity model and a SPICE model is assembled.
Circuit reduction can be done to produce an impedance equivalent circuit model in which the model values can be calculated. The impedance equivalent circuit model can be directly related to the geometry and current paths

## Slide 34: PI Module Overview Part 1 – Concepts and Physics
The PDN problem
Noise on the PDN and an FPGA example
PDN design considerations
A couple of preliminary concepts
Current and inductance physics
A reduced order circuit model from a first principles formulation
Characteristic ZPDN and relationship to physics
  Characteristic ZPDN response resulting from current-path physics and associated inductance
  Relating the ZPDN response to geometry and the impedance equivalent circuit model
  ZPDN frequency response related to physics

## Slide 35: Resulting ZPDN Response
0.001
0.01
0.1
1
10
100
Input Impedance at an IC port [Ω]
0.1
1
10
100
1000
Frequency [MHz]
measurement
Eq. circuit
28 layer PCB
6 layer PCB
VRM
bulk
decaps
0402 decaps
under IC
44 layer PCB
18 layer PCB
Each of these production real PCBs use only a single layer for the power net area fill (with adjacent layers for power return ground).

## Slide 36: Resulting ZPDN Response
6 layer PCB
VRM
bulk
decaps
0402 decaps
under IC
44 layer PCB
ZPDN response is very consistent because of the current path and its associated inductance as seen from the impedance equivalent circuit model
PCB
pkg
IC

## Slide 37: Geometry, Current Path, Model, and ZPDN
Notes: The real board geometry is shown on top. The model and response are shown at bottom right and left respectively. The response for increasing number of capacitors is compared at the bottom left. As number of capacitors increase, the capacitance at low frequency increases as a direct result. Also LEQ , converges into LIC as the capacitors are added. Thus, if LIC is lower, then the LEQ will converge to a lower value. LIC is independent of the capacitors placed on the PCB.

## Slide 38: Frequency Response for PCB PDN - C
Cplane
+CDecap
LPCB_EQ
CPlane
LPCB_IC
GND1
GND3
PWR
GND4
GND6
Labove
Labove
Labove
LPCB_IC
LPCB_Decap
LPCB_Decap
LPCB_Decap
LPCB_Plane
S.C
S.C
S.C

## Slide 39: Frequency Response for PCB PDN – f1
CDecap
LPCB_EQ
CPlane
LPCB_IC
GND1
GND3
PWR
GND4
GND6
Labove
Labove
Labove
LPCB_IC
LPCB_Decap
LPCB_Decap
LPCB_Decap
LPCB_Plane
O.C

## Slide 40: Frequency Response for PCB PDN – LPCB EQ
CDecap
LPCB_EQ
CPlane
LPCB_IC
GND1
GND3
PWR
GND4
GND6
Labove
Labove
Labove
LPCB_IC
LPCB_Decap
LPCB_Decap
LPCB_Decap
LPCB_Plane
S.C
S.C
S.C
O.C

## Slide 41: Frequency Response for PCB PDN – f2
CDecap
LPCB_EQ
CPlane
LPCB_IC
GND1
GND3
PWR
GND4
GND6
Labove
Labove
Labove
LPCB_IC
LPCB_Decap
LPCB_Decap
LPCB_Decap
LPCB_Plane
S.C
S.C
S.C

## Slide 42: Frequency Response for PCB PDN –CPlane
CDecap
LPCB_EQ
CPlane
LPCB_IC
GND1
GND3
PWR
GND4
GND6
Labove
Labove
Labove
LPCB_IC
LPCB_Decap
LPCB_Decap
LPCB_Decap
LPCB_Plane
O.C
O.C
O.C
S.C

## Slide 43: Frequency Response for PCB PDN – f3
CDecap
LPCB_EQ
CPlane
LPCB_IC
GND1
GND3
PWR
GND4
GND6
Labove
Labove
Labove
LPCB_IC
LPCB_Decap
LPCB_Decap
LPCB_Decap
LPCB_Plane
O.C
O.C
O.C
S.C

## Slide 44: Frequency Response for PCB PDN –LPCB IC
CDecap
LPCB_EQ
CPlane
LPCB_IC
GND1
GND3
PWR
GND4
GND6
Labove
Labove
Labove
LPCB_IC
LPCB_Decap
LPCB_Decap
LPCB_Decap
LPCB_Plane
O.C
O.C
O.C
S.C

## Slide 45: Key Points
The shape of the ZPDN curve is very characteristic but relatively simple, even though the geometry of the PDN on a multi-layer PCB is complicated
The current-path physics governing the impedance are dominated by inductance and lumped element resonances above approximately 1 MHz
The inductance is dominated by the current path – geometry “length/area” (series inductance), and the number of parallel paths (parallel inductance) and this will drive the design approach (“small loops and many loops”)
Where power layers are located in stackup
Package ball pitch
Decoupling capacitor interconnect
Number of PWR/GND vias in package
Number of decoupling capacitors

## Slide 46: PI Module Overview Part 1 – Concepts and Physics
The PDN problem
Noise on the PDN and an FPGA example
PDN design considerations
A couple of preliminary concepts
Current and inductance physics
A reduced order circuit model from a first principles formulation
Characteristic ZPDN and relationship to physics
Understanding PDN physics and design through examples
Identifying limiting physics in design
Adding decoupling capacitors

## Slide 47: Power Plane and Capacitor Location Matrix

## Slide 48: Lhigh – Power Plane Location in Layer Stack
Power plane at Top
Power plane Middle
Power plane Bottom
LPCB_IC

## Slide 49: Lhigh – Power Plane Location in Layer Stack
Power plane at Top
Power plane Middle
Power plane Bottom
Decreasing current path and inductance from package balls to PDN power layer net
Power layer closest to the IC minimizes IC to power plane inductance. (Recall that jwLPCB_IC is the impedance limit above a few MHz.)
LPCB_IC

## Slide 50: Lhigh – Power Plane Location in Layer Stack
Power plane at Top
Power plane Middle
Power plane Bottom
?
LPCB_IC
Q: How many power pins are there here?
Q: Why is the mid frequency range impedance not changing

## Slide 51: Capacitor Location – Top, Bottom, at IC
Capacitors placed on the side closest to the power plane reduces the inductance from the capacitor to power plane and LEQ. The current path length/area is smallest.
LPCB_IC
LPCB_EQ

## Slide 52: Capacitor Location – Top, Bottom, at IC
LPCB_EQ
LPCB_IC
Q: Why are there only two curves in the mid-frequency range and what do they correspond to? Explain the differences.

## Slide 53: LEQ – Power Plane Location and Decaps
Power planes – top
Power planes – mid
Power planes – bottom
Power plane at Top
Power plane Middle
Power plane Bottom
LPCB_EQ
LPCB_IC
Consider the IC to have >100 PWR pins (and associated GND return) such that LPCB IC is very small. And that many decaps can be added.
Q: What limits the PDN impedance in each case above?

## Slide 54: Example
Q: What happens if the number of IC pins are doubled?
18 layer PCB
Layer 2 is the power layer
45 power pins, 109 surrounding GND
45 decaps under the IC

## Slide 55: Key Points
The ZPDN response can be related to the geometry, current path and associated inductance.
The dominant component in the impedance equivalent circuit can be identified and used to explain the behavior of the PDN response, and to guide the PDN design.

## Slide 56: PI Module Overview Part 1 – Concepts and Physics
The PDN problem
Noise on the PDN and an FPGA example
PDN design considerations
A couple of preliminary concepts
Current and inductance physics
A reduced order circuit model from a first principles formulation
Characteristic ZPDN and relationship to physics
Understanding PDN physics and design through examples
Identifying limiting physics in design
  LPCB IC
  Decaps under the IC
  All decaps

## Slide 57: LPCB IC Physical Limit
LPCB IC is the physical limit at high frequencies when the current returns through the interplane capacitance of the power net area fill and return
S.C
O.C
O.C
O.C
LPCB IC limit

## Slide 58: Real Board LPCB IC Examples
0.001
0.01
0.1
1
10
100
Input Impedance at an IC port [Ω]
0.1
1
10
100
1000
Frequency [MHz]
measurement
Eq. circuit
28 layer PCB
6 layer PCB
VRM
bulk
decaps
0402 decaps
under IC
44 layer PCB
18 layer PCB

## Slide 59: LPCB IC Physical Limit
LPCB IC is the physical limit at high frequencies when the current returns through the interplane capacitance of the power net area fill and return
S.C
O.C
O.C
O.C
LPCB IC limit

## Slide 60: All Decaps Physical Limit
The All Decaps physical limit is when shorts are placed across all decap locations under the IC, and a ring of many capacitor locations on the top and bottom of the PCB are shorted at the bonding pads
S.C.
S.C.
S.C.
All decaps limit

## Slide 61: Decaps Under the IC Physical Limit
There is a physical limit when all the power pins under the IC are shorted on the bottom layer that corresponds to placing all possible decaps under the IC
Decaps under
the IC limit

## Slide 62: Key Points
Physical limits can be established for the upper bound of placing decoupling capacitors at various locations
  LPCB IC
  Decaps under the IC
  All decaps
If the target impedance cannot be met due to a particular limitation, the nature of the limitation and the impedance equivalent circuit can guide the design direction.

## Slide 63: PI Module Overview Part 1 – Concepts and Physics
The PDN problem
Noise on the PDN and an FPGA example
PDN design considerations
A couple of preliminary concepts
Current and inductance physics
A reduced order circuit model from a first principles formulation
Characteristic ZPDN and relationship to physics
Understanding PDN physics and design through examples
Identifying limiting physics in design
Adding decoupling capacitors
  Values of decaps to use
  Where to place around the IC
  Connecting the decap to the PCB
  Convergence of LPCB Decap for large number of decaps

## Slide 64: Two Approaches for SMT Decoupling
Use an array of capacitor values:
  This may be the best known approach in the signal integrity design community
  Rationale: to maintain a flat impedance profile below a target impedance over a wide frequency range
  Typically a logarithmically spaced (10, 22, 47, 100, 220, 470nF, etc.) array of several values per decade.
Use a large capacitor value in the package size
  This is less well-known, but an approach in the EMI design community
  Rationale: to keep impedance as low as possible, less emphasis on a target impedance and a flat profile

## Slide 65: Decoupling Strategy – Geometry
GND (PWR Return)
PWR
9 in.
6 in.
t=10 mils.
tan d = 0.02
er=4.5

## Slide 66: Approaches for SMT Decoupling Values
Approach A : values of decoupling capacitors logarithmically spaced, i.e. 3 values per decade: 10, 22, 47, 100, etc.
Approach B : largest values of decoupling available in two package sizes, i.e., 0603 and 0402
Approach B1 : largest values of decoupling available in one package size, i.e., 0402.
Target Impedance
Notes: 66

## Slide 67: Optimizing Algorithm –10 decaps
Real 18 layer PCB with a maximum of 45 locations for decaps under the IC
VRM
Bulk
decaps
0402 decaps
under IC

## Slide 68: Optimizing Algorithm –35 decaps
Real 18 layer PCB with a maximum of 45 locations for decaps under the IC
VRM
Bulk
decaps
0402 decaps
under IC

## Slide 69: Optimizing Algorithm –45 decaps
Real 18 layer PCB with a maximum of 45 locations for decaps under the IC
VRM
Bulk
decaps
0402 decaps
under IC

## Slide 70: 28 Layer Real PCB Design: 1 Capacitor
C1210 (0603)
Measurement
Circuit Model
0.1
1
10
100
1000
0.001
0.01
0.1
1
10
100
Input Impedance at an IC port [Ω]
Frequency [MHz]
IC port
0.1
1
10
100
1000
0.001
0.01
0.1
1
10
100
Input Impedance at an IC port [Ω]
Frequency [MHz]

## Slide 71: 28 Layer Real PCB Design: 19 Capacitors
19 Decaps
Measurement
Circuit Model
IC port
0.001
0.01
0.1
1
10
100
Input Impedance at an IC port [Ω]
0.1
1
10
100
1000
Frequency [MHz]

## Slide 72: 28 Layer Real PCB Design: 43 Capacitors
19 Decap
7 Decap
17 Decap
IC
Measurement
Circuit Model
Input Impedance at an IC port [Ω]
0.001
0.01
0.1
1
10
100
Input Impedance at an IC port [Ω]
0.1
1
10
100
1000
Frequency [MHz]

## Slide 73: Key Points
Decoupling capacitors can be added using several values in a given decade to decouple over wide frequency ranges
Decoupling capacitors can be added as the largest value in a package size to achieve a target impedance as well.

## Slide 74: PI Module Overview Part 1 – Concepts and Physics
The PDN problem
Noise on the PDN and an FPGA example
PDN design considerations
A couple of preliminary concepts
Current and inductance physics
A reduced order circuit model from a first principles formulation
Characteristic ZPDN and relationship to physics
Understanding PDN physics and design through examples
Identifying limiting physics in design
Adding decoupling capacitors
  Values of decaps to use
  Where to place around the IC
  Connecting the decap to the PCB
  Convergence of LPCB Decap for large number of decaps

## Slide 75: LPCB_Plane Current Physics and Inductance
D
8”x8”
10
0
10
1
10
-1
Number of Decaps
LPCB_Plane [nH]
1 IC Pin
4 IC Pin
8 IC Pin
16 IC Pin
32 IC Pin
LPCB_Plane decreases with multiple parallel paths
10
3
10
-2
10
-1
D[mils]
Lplane [nH]
LPCB_Plane vs D
32 IC 32 Decap
32 IC 8 Decap
32 IC 1 Decap
D
8”x8”
D=1’’, Pitch = 1mm
Decaps are placed on the top layer

## Slide 76: LPCB_Plane Current Physics and Inductance
D
8”x8
10
0
10
1
10
-1
Number of Decaps
LPCB_Plane [nH]
1 IC Pin
4 IC Pin
8 IC Pin
16 IC Pin
32 IC Pin
10
3
10
-2
10
-1
D[mils]
Lplane [nH]
LPCB_Plane vs D
32 IC 32 Decap
32 IC 8 Decap
32 IC 1 Decap
D
8”x8”
Q: When is placing capacitors in a ring around the IC most beneficial?

## Slide 77: Current Path, and Inductance
Q: If the current path from IC to the decaps is not in direct line (e.g., crosses a cutout or slot, goes around a corners, etc.), which portion of the inductance is affected, and can potentially become dominant?
Notes: The real board geometry is shown on top. The model and response are shown at bottom right and left respectively. The response for increasing number of capacitors is compared at the bottom left. As number of capacitors increase, the capacitance at low frequency increases as a direct result. Also LEQ , converges into LIC as the capacitors are added. Thus, if LIC is lower, then the LEQ will converge to a lower value. LIC is independent of the capacitors placed on the PCB.

## Slide 78: Key Points
If LPCB Plane is dominant, e.g., when the power net area fill is near the top, and the decaps are placed on the top layer, then placing the capacitors in a ring around the IC can minimize LPCB Plane
In general, LPCB Plane is typically not the limiting factor, and decaps are often limited to “keep-in” regions where signal routing channels are not compromised.

## Slide 79: PI Module Overview Part 1 – Concepts and Physics
The PDN problem
Noise on the PDN and an FPGA example
PDN design considerations
A couple of preliminary concepts
Current and inductance physics
A reduced order circuit model from a first principles formulation
Characteristic ZPDN and relationship to physics
Understanding PDN physics and design through examples
Identifying limiting physics in design
Adding decoupling capacitors
  Values of decaps to use
  Where to place around the IC
  Connecting the decap to the PCB
  Convergence of LPCB Decap for large number of decaps

## Slide 80: Practices for Mounting SMT Capacitors
best
ok
poor
Adding trace length, adds inductance to the interconnect:
“loop area” above the planes – Labove
Area between the power and GND return vias vertically connecting to the PWR planes
PWR via
GND via
PWR current
Return current
practical

## Slide 81: Example 1: The Doublet – Minimizing LPCB Decap
GND via
PWR via
Placing decaps on in pairs allows to use mutual inductance to minimize overall LPCB Decap
Q: If LPCB IC is negligible, in which cases can the doublet configuration be beneficial? Which cases less so.

## Slide 82: Example 2: The Doublet – Minimizing LPCB Decap
GND via
PWR via
Placing decaps on in pairs allows to use mutual inductance to minimize overall LPCB Decap
Q: If LPCB IC is negligible, and decaps can be placed under the IC, in which cases can the doublet configuration be beneficial? Which cases less so.
Q: Which of these cases is not well chosen for the decap location?
doublet
doublet
doublet

## Slide 83: PI Module Overview Part 1 – Concepts and Physics
The PDN problem
Noise on the PDN and an FPGA example
PDN design considerations
A couple of preliminary concepts
Current and inductance physics
A reduced order circuit model from a first principles formulation
Characteristic ZPDN and relationship to physics
Understanding PDN physics and design through examples
Identifying limiting physics in design
Adding decoupling capacitors
  Values of decaps to use
  Where to place around the IC
  Connecting the decap to the PCB
  Convergence of LPCB Decap for large number of decaps

## Slide 84: LPCB_Decap Convergence
IC Region
5’’x 6’’
D
D
Alternating
Aligned
Doublet
convergence rate for all SMT package sizes
*The LPCB_Decap is simulated in PDN Tool and the inductance is extracted from |ZPDN|.

## Slide 85: LPCB_Decap Capacitor Configuration Example
Doublet: 8 pairs
Alternating: 14 pairs
1/n: 25 pairs (no mutual coupling between individual decaps)
Aligned: 30 pairs
IC Region
5’’x 6’’
D
D
Alternating
Aligned
Doublet

## Slide 86: Key Points
Adding capacitors decreases LPCB Decap as 1/n
Geometries such as the Doublet or 3-terminal capacitors reduce inductance over geometries where there is no benefit of mutual inductance.

## Slide 87: Design Implications
Use the impedance equivalent circuit model to try to identify what component is dominant and use it to guide meeting the target impedance.
PWR/GND plane pair nearer to the IC in stackup will minimize LPCB_IC from package balls to power net area fill (smaller loop)
PWR/GND plane pairs closely spaced will reduce LPCB_plane.
Place caps close to the power layer to minimize the inductance from the capacitor to the power net area fill layer, i.e., LPCB_decaps. (minimize the loop)
Placing caps on the underside of PCB opposite package can benefit the design
  The space is available and requires no additional vias
  If the pkg/planes/decap path is shorter due to PWR/GND near package in stackup decaps around the IC will be more effective
Power and ground vias placed adjacent to the caps reduces the inductance in the current return path (or in the bonding pads). (smaller loops)
Capacitor arrangements that utilize mutual inductance, e.g., doublet, or 3-terminal capacitor, can significantly reduce LPCB_decaps.

## Slide 88
Thank you!