## Slide 1: Power Integrity for High-Speed Design on Multi-Layer PCBs Concepts and Physics
James L. Drewniak
Clear Signal Solutions and
Missouri S&T EMC Laboratory
james.drewniak@clearsig.com

## Slide 2: Contributors
IBM – B. Archambeault, S. Connor, M. Cocchini, W. Becker, M. Cracraft, A. Ruehli
Cisco – B. Achkir, S. Scearce, Q. Gaumer, M. Sapazhnikov
Missouri S&T – B. Zhao, S. Bai, S. Liang, X. Zhu, K. Shringapure, S. Pan, J. Xu, J. Fan

## Slide 3: Overview – Pre-layout Methodology
Problem and concepts
PDN pre-layout design methodology
Circuit model
Example
Silicon Die
LPCB_IC
Labove
LPCB_Decap

## Slide 4: Problem Introduction
VDD
Time
Vripple
Voltage
package
PowerSI
SIwave
PiPro
…
…

## Slide 5: A Systematic Approach for Achieving PI
log10f
pkg vias to IC
pkg+ on-pkg decap
PCB vias to pkg
PCB + board decoupling
low-frequency capacitance
no on package decoupling
On-die capacitance
PCB

## Slide 6: PDN Design Considerations
IC
IC pins
Decaps
PWR
GND
Power/ground net area fill
Location in stack
Spacing to power return plane
Total area fill
Special materials
Effect of other ground/reference planes?
2a. Decoupling capacitors
Top
Bottom,
Beneath IC?
2b. Decoupling capacitor connection -
PWR/GND via geometry
Package size
2c. Decoupling capacitor layout
How close to IC?
Shape – ring IC, on one side?
2a. Decoupling capacitors
Value(s)
Number (total C)
3. IC PWR/GND
Number pins
Pin pattern
Pitch
On-package decaps
The pre-layout methodology is for multi-layered PCB PDN geometry.
Notes: How to achieve a target impedance:
Power plane
Decoupling capacitors
IC pins

## Slide 7: PI Design Flow – Package

## Slide 8: Design Flow – PCB

## Slide 9: Objective: PCB Impedance Equivalent Circuit
Ri
LPCB_IC
LPCB_Decap_i
Labove_i
G
Cdecap_i
CPlane
…
LPCB_Plane
Objective: Determine the values for:
  LPCB_IC calculation
  LPCB_plane calculation
  LPCB_decap calculation
  Labove calculation
  Calculate ZPND and voltage ripple
Can add package, IC, and VRM models to this

## Slide 10: Overview – Pre-layout Methodology
Problem and concepts
PDN pre-layout design methodology
  Example geometry
  LPCB_IC calculation
  LPCB_decap calculation
  LPCB_plane calculation
  Labove calculation
Silicon Die
LPCB_IC
Labove
LPCB_Decap

## Slide 11: PCB PDN Example - Geometry
IC Region
5’’x 6’’
D
D
Doublet
Alternating
1.2mils
1.2mils
1.2mils
1.2mils
2.4mils
2.4mils
2.4mils
1.2mils
1.2mils
1.2mils
1.2mils
1.2mils
1.2mils
1.2mils
1.2mils
1.2mils
G1-GND
S2-SIG
G3-GND
S4-SIG
G5-GND
P6-PWR
G7-GND
S8-SIG
G9-GND
S10-SIG
G11-GND
S12-SIG
G13-GND
S14-SIG
G15-GND
G16-GND
5mils
5mils
8mils
8mils
8mils
5mils
5mils
15mils
5mils
8mils
5mils
8mils
5mils
8mils
5mils
IC pin
Decap
Decap
Decap

## Slide 12: Overview – Pre-layout Methodology
Problem and concepts
PDN pre-layout design methodology
  Example geometry
  LPCB_IC calculation
  LPCB_decap calculation
  LPCB_plane calculation
  Labove calculation
Silicon Die
LPCB_IC
Labove
LPCB_Decap

## Slide 13: LPCB_IC Geometry
Pitch | Drill size | Anti-pad size
1 mm | 8mils | 20mils
 | 12mils | 32mils
 | 15mils | 39mils
0.8 mm | 8mils | 20mils
 | 12mils | 20mils
h
port
short
…
Row
Hex
Hex1
Alternating
Grid
GND via
PWR via
Pitch
Drill size
Pad size
Anti-pad size

## Slide 14: LPCB_IC Inductance Physics – goes as h
GND1
PIC1
GND2
GND3
PIC2
PIC3
PIC4
Connection to Power/ground cavity (internal port )
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
Pi1
Pi2
Pi3
Pi4
IC Port
GND1
GND2
GND3
Cavity Model
Calculate a per-unit-layer inductance

## Slide 15: LPCB_IC Convergence for 1mm Pitch
512

## Slide 16: LPCB_IC Caclulation
Calculate inductance of 1 cell
Get any other number of pins as 1/n

## Slide 17: LPCB_IC Design Calculations
Pitch | Drill size | 1/n | 1/nUnitCell
1 mm | 8mils | 24.5 | 13.5
 | 12mils | 20.4 | 11.0
 | 15 mils | 18 | 9.5
0.8 mm | 8mils | 22.0 | 12.0
 | 12mils | 17.9 | 9.5
LPCB_IC per mil for one IC pin [pH]
IC Port
GND1
GND2
GND3
All mutual inductances are accounted for
Layers are “in series”

## Slide 18: LPCB_IC Design Calculations per-unit-layer

## Slide 19: LPCB_IC Design Flow
Use the IC pin placement with the lowest n=1 inductance
Adjust the stack-up to reduce the height from the IC port to the power net area fill
Approximate the range of the LPCB_IC using the 1/n and 1/nUnitCell value to meet the high-frequency target impedance
Calculate the # of IC pins needed according to the 1/n and 1/nUnitCell curve for the geometry
LPCB_IC
Target Impedance
Minimal possible L
Frequency
Cplane
LPCB_EQ
Cdecap

## Slide 20: LPCB_IC Example
G1-GND
S2-SIG
G3-GND
S4-SIG
G5-GND
P6-PWR
G7-GND
S8-SIG
G9-GND
S10-SIG
G11-GND
S12-SIG
G13-GND
S14-SIG
G15-GND
G16-GND
5mils
5mils
8mils
8mils
8mils
5mils
5mils
15mils
5mils
8mils
5mils
8mils
5mils
8mils
5mils
IC pin
Decap
Decap
Decap
LPCB_IC
Alternating
Drill size = 15mils,
Anti-pad size = 39mils,
Pitch = 1mm.
Requirement:
The IC pin # is 32, given by package designer.

## Slide 21: Impedance Equivalent Circuit
Ri
LPCB_IC=14.6pH
LPCB_Decap_i
Labove_i
G
Cdecap_i
CPlane
…
LPCB_Plane

## Slide 22: LPCB_EQ Components Approximation
CDecap
LPCB_EQ
CPlane
LPCB_IC
Target Impedance
Frequency
|ZPDN|
LPCB_IC=14.6 pH
Lhigh_needed=79.6 pH
LPCB_EQ_min=79.6pH
Assume: LPCB_Decap is the similar to Labove, LPCB_Plane
LPCB_Decap = 22pH,
LPCB_above = 22pH,
LPCB_Plane = 22pH.

## Slide 23: Overview – Pre-layout Methodology
Problem and concepts
PDN pre-layout design methodology
  Example geometry
  LPCB_IC calculation
  LPCB_decap calculation
  LPCB_plane calculation
  Labove calculation
Silicon Die
LPCB_IC
Labove
LPCB_Decap

## Slide 24: LPCB_Decap Geometry
Alternating
Aligned
Doublet
Placement pattern | Size | a | b | X | Y
Alternating/Aligned | 0201 | 45 | 120 | 159 | 85
 | 0402 | 53 | 136 | 175 | 101
 | 0603 | 88 | 207 | 246 | 171
 | 0805 | 108 | 223 | 262 | 211
Doublet | 0201 | 32 | 32 | 149 | 71
 | 0402 |  |  | 165 | 87
 | 0603 |  |  | 235 | 158
 | 0805 |  |  | 275 | 174
Relative via locations and package size ([mils]) of the three decoupling capacitor placement patterns
a
b
X
Y
a
b
X
Y
X
Y
b
a
Occupied area
Solder land
Solder resist pattern
Package area

## Slide 25: LPCB_Decap Inductance Physics
Coupling between IC via and decap via neglected
IC vias and decoupling capacitor vias can be modeled separately
GND1
GND2
GND3
Pdecap1
+
-
+
-
+
-
+
-
Pi1
Pi2
Pdecap2
M neglected
due to large distance
M
IC Port
LPCB_Decap

## Slide 26: LPCB_Decap Inductance Physics
Decap 0201, h=40mils | Aligned | Alternating | Doublet
LPCB_Decap¦nDecapPair=1 | 798pH | 372pH | 246pH
Cavity model
Alternating
Aligned
Doublet
Mutual inductance between the PWR and GND vias for one decap
Mutual inductance between the PWR and PWR, or between GND and GND vias in different decaps
Mutual inductance between the PWR and GND, or between PWR and GND vias in different decaps
The sign shows the contributions of the mutual inductances

## Slide 27: LPCB_Decap Functional Variation
IC Region
5’’x 6’’
D
D
Alternating
Aligned
Doublet
convergence rate for all SMT package sizes
*The LPCB_Decap is simulated in PDN Tool and the inductance is extracted from |ZPDN|.

## Slide 28: LPCB_Decap Convergence
convergence rate for all SMT package sizes
Calculate inductance of 1pair
Get any other number of pins as 1/n

## Slide 29: LPCB_Decap Design Calculations
LPCB_Decap_PUL¦npair=1 | Aligned | Alternating | Doublet | Single decap /2
0201 | 20.8 | 11.3 | 6.8 | 14.6
0402 | 21.4 | 11.8 | 6.8 | 15.3
0603 | 23.4 | 14.6 | 6.8 | 17.4
0805 | 23.4 | 15.5 | 6.8 | 17.8
LDecap_above
LPCB_Decap
Distance
LPCB_Decap per mil for one decap pair [pH]

## Slide 30: LPCB_Decap Design Considerations
Use the decap placement with the lowest LPCB_Decap value
Based on the stack-up, place the decaps on bottom or top layer closer to the power net area fill layer (to make the loop area of the decap interconnect smallest)
Calculate the # of decaps needed to achieve LPCB_EQ below the target impedance
Doublet

## Slide 31: LPCB_Decap Design Example
G1-GND
S2-SIG
G3-GND
S4-SIG
G5-GND
P6-PWR
G7-GND
S8-SIG
G9-GND
S10-SIG
G11-GND
S12-SIG
G13-GND
S14-SIG
G15-GND
G16-GND
5mils
5mils
8mils
8mils
8mils
5mils
5mils
15mils
5mils
8mils
5mils
8mils
5mils
8mils
5mils
IC pin
Decap
Decap
LPCB_Decap
Doublet
Requirement LPCB_Decap <= 22 pH

## Slide 32: Impedance Equivalent Circuit
Ri
LPCB_IC=14. 6pH
LPCB_Decap_i
Labove_i
G
Cdecap_i
CPlane
…
LPCB_Plane
LPCB_Decap_i=177 pH (pair)
8 decap pairs

## Slide 33: Decaps Under the IC
GND1
GND2
GND3
GND4
GND5
GND6
PWR
IC Port
GND1
GND2
GND3
GND6
GND5
GND4
PWR

## Slide 34: LPCB_EQ Variation for Decaps Under the IC
Alternating
Grid
LPCB_IC
LPCB_Plane
LPCB_Decap
*The LPCB_EQ is simulated and the inductance is extracted from |ZPDN|.
(Grid)
LPCB_EQ vs # of decaps on IC pins

## Slide 35: LPCB_EQ Example for Decaps Under the IC
G1-GND
S2-SIG
G3-GND
S4-SIG
G5-GND
P6-PWR
G7-GND
S8-SIG
G9-GND
S10-SIG
G11-GND
S12-SIG
G13-GND
S14-SIG
G15-GND
G16-GND
5mils
5mils
8mils
8mils
8mils
5mils
5mils
15mils
5mils
8mils
5mils
8mils
5mils
8mils
5mils
IC pin
Decap
LPCB_IC
Alternating
Drill size = 15mils,
Anti-pad size = 39mils,
Pitch = 1mm.
LPCB_Plane
LPCB_Decap
Design Library ( under development)

## Slide 36: Outline
Problem and concepts
PDN pre-layout design methodology
  Example geometry
  LPCB_IC calculation
  LPCB_decap calculation
  LPCB_plane calculation
  Labove calculation
Silicon Die
LPCB_IC
Labove
LPCB_Decap

## Slide 37: LPCB_Plane Geometry
If the current path on the power net is direct to decaps and L is not significantly changed due to power net voids, the following design curves are used.
Horizontal inductance and vertical inductance are merged in the model and final equivalent circuit model is constructed as below.
GND3
PWR
GND4
IC via
Cavity model can
well estimate the inductance.
GND3
PWR
GND4
Decaps
IC vias
Decap vias

## Slide 38: LPCB_Plane Geometry
D=1’’, Pitch = 1mm
IC Region
GND3
GND4
PWR
Port
Short
Short
Short
D
8”x8”
D
8”x8”
Decaps
Doublet
Stack-up
GND via
PWR via

## Slide 39: LPCB_Plane Current Physics and Inductance
D
8”x8”
10
0
10
1
10
-1
Number of Decaps
LPCB_Plane [nH]
1 IC Pin
4 IC Pin
8 IC Pin
16 IC Pin
32 IC Pin
LPCB_Plane decreases with multiple parallel paths
10
3
10
-2
10
-1
D[mils]
Lplane [nH]
LPCB_Plane vs D
32 IC 32 Decap
32 IC 8 Decap
32 IC 1 Decap
D
8”x8”
Pitch = 1mm
Decaps are placed on the top layer
D=1’’

## Slide 40: LPCB_Plane Design Curves
IC Region
5’’x 6’’
D
D
Doublet
Alternating

## Slide 41: LPCB_Plane Example
IC Region
5’’x 6’’
D
D
Requirement: LPCB_Plane <=22 pH
From the design curves, D=500mils, nDecap_Pair >=16.
Combine the requirement from LPCB_IC, LPCB_Decap, nICpin >=6, nDecap_Pair >=8
nICpin =32, nDecap_Pair >=16

## Slide 42: Impedance Equivalent Circuit
Ri
LPCB_IC=14. 6 pH
LPCB_Decap_i
Labove_i
G
Cdecap_i
CPlane
…
LPCB_Plane=22 pH
LPCB_Decap_i=177 pH (pair)
16 pairs decaps

## Slide 43: Outline
Problem and concepts
PDN pre-layout design methodology
  Example geometry
  LPCB_IC calculation
  LPCB_decap calculation
  LPCB_plane calculation
  Labove calculation
Silicon Die
LPCB_IC
Labove
LPCB_Decap

## Slide 44: Labove Geometry
Top view of doublet pad
(shorted pad )
Power
Ground
Labove
GND1
short
GND1

Labove
PEEC method used to calculate decap pad inductance
Get a single inductance
+
-
Pdecap
LDecap_above
LPCB_Decap
Distance

## Slide 45: Labove Geometries
Decoupling capacitor of sizes 0805/0603/0402/0201 for Labove design space
# | Name | Figure | # | Name | Figure | # | Name | Figure
1 | Shared Via |  | 2 | Power Via Alternating |  | 3 | Doublet | 
4 | Via in Pad |  | 5 | Shared Pad |  | 6 | Via in pad alternating | 
7 | PWR via in Line |  | 8 | 3-terminal |  | 9 | Multi-via | 
100
40
27
50
24
19
12
40
[mil]
Port
GND
2.4
6.7
1.2
[mil]
shorted

## Slide 46: Labove Design Library - Doublet
With Different package sizes,
0201, 0402, 0603, 0805
Using wider trace to minimize inductance
Anti-Pad Diameter: 0.762mm
Pad Diameter: 0.538mm
Via Diameter (drill size): 0.25mm
What will change | 0201 | 0402 | 0603 | 0805
L |  | 56 mil | 78 mil | 100 mil
W |  | 20 mil | 30 mil | 50 mil
gap1 |  | 18 mil | 18 mil | 12 mil
gap2 |  | 15 mil | 15 mil | 21 mil
dis1 |  | 12 mil | 20 mil | 31 mil
dis2 |  | 17 mil | 22 mil | 30 mil
What will not change | 0201, 0402, 0603, 0805
pitch | 1 mm
1mm
L
gap1
gap2
dis2
1mm
W
dis1
gap1

## Slide 47: Labove Design Library - Doublet
Distance (mil) | 0805 | 0603 | 0402
3.5 | 125.6 | 123.8 | 132.9
5 | 161 | 157.4 | 166.2
10 | 248.2 | 239.9 | 244.6
15 | 313.2 | 301.4 | 302.2
20 | 368.4 | 354.3 | 352.3
25 | 419.2 | 403.4 | 399.4
30 | 467.5 | 450.4 | 445
Design Curve
Labove for doublet layout [pH]
Distance
Short
GND
Side view
Port
Short
Port

## Slide 48: Labove Design Library – Power Via Alternating
Dis =10 mils
L
W
gap
What will change | 0201 | 0402 | 0603 | 0805
L |  | 56 mil | 78 mil | 100 mil
W |  | 20 mil | 30 mil | 50 mil
gap |  | 10.5 mil | 11 mil | 11 mil
What will not change | 0201, 0402, 0603, 0805
Dis (Pad Edge to Via ) | 10 mils (0.25 mm)
Anti-Pad Diameter: 0.762mm
Pad Diameter: 0.538mm
Via Diameter (drill size): 0.25mm
With Different package sizes,
0201, 0402, 0603, 0805
Using wider trace to minimize inductance
Power Via
Ground Via

## Slide 49: Labove Design Library – Power Via Alternating
Design Curve
Labove for alternating layout [pH]
Distance (mil) | 0805 | 0603 | 0402
3.5 | 124.3 | 142.4 | 147.7
5 | 164.2 | 181.1 | 179.1
10 | 274.5 | 280.1 | 257.9
15 | 364.7 | 355.9 | 317.7
20 | 444.1 | 421.1 | 369.6
25 | 517.2 | 480.8 | 418.2
30 | 586.8 | 537.4 | 464.7
Distance
gap=0.3 mm
Short
GND
Side view
Port
Short
Port

## Slide 50: Labove Design Library – Power Via Aligned
Dis =10 mils
L
W
gap
What will change | 0201 | 0402 | 0603 | 0805
L |  | 56 mil | 78 mil | 100 mil
W |  | 20 mil | 30 mil | 50 mil
gap |  | 10.5 mil | 11 mil | 11 mil
With Different package sizes,
0201, 0402, 0603, 0805
Using wider trace to minimize inductance
What will not change | 0201, 0402, 0603, 0805
Dis (Pad Edge to Via ) | 10 mils (0.25 mm)
Anti-Pad Diameter: 0.762mm
Pad Diameter: 0.538mm
Via Diameter (drill size): 0.25mm
Power Via
Ground Via

## Slide 51: Labove Design Library – Power Via Aligned
Design Curve
Labove for aligned layout [pH]
Distance (mil) | 0805 | 0603 | 0402
3.5 | 132.4 | 157.3 | 172.4
5 | 180.1 | 208.1 | 217.8
10 | 327.8 | 360.3 | 354.8
15 | 464.7 | 497.8 | 478.4
20 | 595 | 626.8 | 594.5
25 | 721.3 | 749.8 | 705.4
30 | 842.8 | 868.8 | 812.9
Distance
gap=0.3 mm
Short
GND
Side view
Port
Short
Port

## Slide 52: Labove Modeling with Decaps
GND
Wave Port
Decoupling capacitor
Via, pad, trace, one decap
Decoupling capacitor model
Define Distance’=Distance +½*H,
Change the plane to the center of the capacitor (without including Decap in the model).
Decap
Via
Distance
H

## Slide 53: Labove Modeling
Distance (mil) | Inductance (pH) | Distance’ | Inductance (pH) | Difference
5 | 615.34 | 5+H/2 | 602.32 | 2.12%
8 | 677.26 | 8+H/2 | 655.07 | 3.26%
15 | 883.43 | 15+H/2 | 828.04 | 6.27%
0402 Type Decap
Decap
Distance
H=20 mil
Distance+H/2
Distance
Distance+H/2
CST
Model

## Slide 54: Labove Example
Pick doublet 0805 layout for Labove calculation with distance = 5mils, and decap body height H = 10mils. Then distance + H/2=10mils. From the library, the Labove for one decap is
Decap
Via
Distance
H
LDecap_above
LPCB_Decap
From previous design: nICpin =32, nDecap_Pair >=16,
Requirement: LPCB_Decap +Labove = 22pH+22pH=44pH

## Slide 55: Impedance Equivalent Circuit
Ri
LPCB_IC=14. 6pH
LPCB_Decap_i
Labove_i
G
Cdecap_i
CPlane
…
LPCB_Plane=22 pH
LPCB_Decap_i=177 pH (pair)
16 pairs decaps
Labove_i= 248 pH (pair)

## Slide 56: Outline
Problem and concepts
PDN pre-layout design methodology
Circuit model and example
Silicon Die
LPCB_IC
Labove
LPCB_Decap

## Slide 57: Impedance Equivalent Circuit
Ri
LPCB_IC=14. 6pH
LPCB_Decap_i
Labove_i
G
Cdecap_i
CPlane
…
LPCB_Plane=22 pH
LPCB_Decap_i=177 pH (pair)
16 pairs decaps
Labove_i= 248 pH (pair)

## Slide 58: PCB Example
PCB PDN Design:
32 IC pins
D = 500mils
16 pairs of decaps using doublet layout on the top layer

## Slide 59: PCB Example Input Impedance
LPCB_EQ = 60pH
LPCB_IC = 14.6pH
For 0805 decap, ESR =30mOhm
For 16 decap pairs, REQ is around 30mOhm/32 =0.94mOhm.
Gdiel = 0.1S from real board measurement
RIC = 0.01Ohm from real board measurement
Assume the decap is 100nF, CDecap = 3.2uF
CPlane = 2.7 nF
Target Impedance
HSpice simulation

## Slide 60
Thank You!